## Slide 1: Enhanced Gateway Multipoint Relays for Constructing a Small Connected Dominating Set in Wireless Ad Hoc Networks
Ou Liang, Ahmet Sekercioglu and Nallasamy Mani
Department of Electrical and Computer Systems Engineering
Monash University, Australia

## Slide 2: Sections
An overview of Gateway Multipoint Relays (GMPR).
A drawback of GMPR.
Our enhancement.
Conclusion.

## Slide 3: Gateway Multipoint Relays (GMPR)
It’s a combination of clustering and Multipoint Relays methods.
Each node can be in one of the four states: Dominator, Dominatee, connector, candidate.
Dominators and connectors create a connected dominating set (CDS) in the network.
Only nodes in the CDS retransmit broadcast packets.
Section 1
Section 2
Section 3
Section 4

## Slide 4: Connected dominating set (CDS)
Section 1
Section 2
Section 3
Section 4
A CDS is a set of nodes where all nodes in the network are either in the CDS or have at least one neighbor node in the CDS. The graph induced by nodes in the CDS is connected.
D
B
F
A
E
C
G
H
I
J
O
P
N
L
K
M
T
The CDS contains:
{ D, F, H, J, K, P }

## Slide 5: Operations of GMPR
Section 1
Section 2
Section 3
Section 4
Select dominators to cover all nodes in the network (Dominators are not connected at this stage).
Each dominator performs MPR calculation to select MPRs to cover all its two-hop neighbor nodes.
An MPR is a connector if it has been selected by the largest dominator (largest node degree) in its one-hop neighborhood.
After establishing connectors, each dominator apply a self-pruning procedure to decide whether it is a silent-dominator.

## Slide 6: Self-pruning procedure
Aim: To remove leaf-dominators.
A dominator D is a leaf-dominator if there exists a connector in D’s one-hop neighborhood, which can cover all D’s one-hop neighbors.
A leaf-dominator is referred to as the silent-dominator, which still selects MPRs but does not retransmit broadcast packets.
Section 1
Section 2
Section 3
Section 4

## Slide 7: Self-pruning procedure example
G
A
D
E
H
F
I
B
C
After selecting connectors
Dominators: E, H
Connector: F
Then Both dominators apply self-pruning procedure, and H becomes a silent-dominator.
Section 1
Section 2
Section 3
Section 4

## Slide 8: A drawback of GMPR
Section 1
Section 2
Section 3
Section 4
We found that the self-pruning procedure used in the GMPR algorithm is insufficient in many occasions.
F
A
E
D
B
C
Connector
Dominator
Node E will not change to a silent-dominator
Insufficiency of the self-pruning procedure

## Slide 9: Our enhancement
Aim:
To enhance the self-pruning procedure to achieve more sufficiency while keeping the algorithm’s computation complexity low.
Section 1
Section 2
Section 3
Section 4
F
A
E
D
B
C
Insufficiency of the self-pruning procedure

## Slide 10: Modify signaling messages
Section 1
Section 2
Section 3
Section 4
IDs of MPRs
IDs of one-hop neighbors
MPR algorithm signaling message
O(Δ)
O(Δ)
State
IDs of MPRs
IDs of one-hop neighbors
GMPR signaling message
O(Δ)
O(Δ)
2 bits
Dominator
Other states
State
IDs of one-hop neighbors
O(Δ)
2 bits

## Slide 11: Modify signaling message
Section 1
Section 2
Section 3
Section 4
Enhanced GMPR signaling message
State
IDs of MPRs
IDs of one-hop neighbors
O(Δ)
O(Δ)
2 bits
Dominator
Connector &
dominatee
State
O(Δ)
2 bits
Largest
dominator
IDs of one-hop neighbors
4bytes
Candidate
State
O(Δ)
2 bits
IDs of one-hop neighbors

## Slide 12: A new self-pruning procedure
Section 1
Section 2
Section 3
Section 4
Rule:
A dominator E is a silent-dominator if all its one-hop neighbors can be covered by a two-hop away dominator A and its connectors, where A has larger node degree than E.
F
A
E
D
B
C
F is selected by A, and A is the largest dominator in F’s one-hop neighborhood.
Largest dominator is A
Largest dominator is A
I am
a silent-dominator

## Slide 13: Simulation studies
Section 1
Section 2
Section 3
Section 4
Simulator | OMNeT++ with Mobility Framework
MAC protocol | Assume a perfect MAC layer (error and collision free).
Network area | 100m x 100m two dimensional area.
Topology generating | Randomly distribute nodes in the area. Each node is placed within the transmission range of a previously placed node to make sure connectivity.
Number of nodes | from 20 to 100 with 10 interval
Transmission range | Two transmission ranges: 25m and 50m
Number of runs | A sufficient number of runs are conducted to achieve 95% confidence interval within a ±5% margin.

## Slide 14: Simulation results (CDS size)
Section 1
Section 2
Section 3
Section 4
Transmission range R = 25m
Transmission range R = 50m

## Slide 15: Simulation results (signaling message size)
Section 1
Section 2
Section 3
Section 4
Transmission range R = 25m
Transmission range R = 50m

## Slide 16: Conclusion
We enhanced the Gateway Multipoint Relays algorithm by modifying the signaling message and the self-pruning procedure. Simulation studies show that our enhanced GMPR algorithm can sufficiently remove leaf-dominators while still keeping a low message size.
Section 1
Section 2
Section 3
Section 4

## Slide 17: Questions?

## Slide 18: Thank you!